## Slide 1: Decrypt Wireless Packets
Traffic files: https://github.com/frankwxu/digital-forensics-lab/tree/main/Illegal_Possession_Images/lab_files/wlan_decrypt
Notes: https://github.com/ctfs/write-ups-2015/tree/master/codegate-ctf-2015/programming/good-crypto
https://www.mathyvanhoef.com/2015/03/codegate-2015-goodcrypto-advanced-wep.html

## Slide 2: Overview
Decrypt traffic
  Find the security key
  Decrypt traffics using a security key
    wlan packets saved in .pcap
  Extract files from packets
Crack wifi password
  IEEE 802.11 and Motivation
  What is Wired Equivalent Privacy?

## Slide 3: Decrypt traffics
Date credits: CodeGate General Capture the flag challenge (CTF) 2015

## Slide 4: Goal: only use a secret key (IV unknown) to decrypt encrypted payload
Problem with Stream Cipher
Consider two packets with the same IV ⇒ Same keystream b
c1 = p1 ⊕ k; c2 = p2 ⊕ k
  ⇒ c1 ⊕ c2=p1 ⊕ p2
two packets with the same IV
  ⇒ XOR = Difference in plain text
50% chance of using the same IV in 4823 packets.
Recovered ICV matches ⇒ Plain text is correct
Possible to recover all 224 keystreams in a few hours
Notes: https://www.cse.wustl.edu/~jain/cse571-09/ftp/l_19wls.pdf

## Slide 5
Create a working space
Download a traffic file
Notes: wget https://raw.githubusercontent.com/ctfs/write-ups-2015/master/codegate-ctf-2015/programming/good-crypto/file.xz

## Slide 6
Unzip the file
Capture the flag challenge
CodeGate General CTF 2015

## Slide 7
Show the encrypted traffic
Notes: https://www.vnsecurity.net/ctf%20-%20clgt%20crew/2015/03/16/codegate-good-crypto.html

## Slide 8
Find key
key length 40 bits
Notes: sudo apt install aircrack-ng
aircrack-ng file

## Slide 9
Decrypts traffic with the key
Notes: airdecap-ng -w A43DF6F374 file

## Slide 11: Extract files from packets

## Slide 12
"Foremost" is a popular open-source forensic tool used for data recovery on the Linux operating system
Carving files from traffic

## Slide 13
Show extracted files
Notes: http://www.blackhat.com/presentations/bh-usa-01/TimNewsham/bh-usa-01-Tim-Newsham.ppt

## Slide 14: Crack wifi password

## Slide 15: Where does 802.11 fit in the OSI Model?
(Ethernet) and 802.11 (WiFi) data and physical layers
https://hpbn.co/wifi/
Notes: https://microchipdeveloper.com/wifi:80211-osi

## Slide 16: IEEE 802.11
802.11 is a set of standards for wireless networking that defines how wireless devices communicate with each other.
The 802.11 standards define the format of data frames, which are the units of data that are transmitted between devices.
There are several types of 802.11 frames, including management frames, control frames, and data frames.
  Management frames: manage the wireless network, such as establishing and maintaining a connection, authenticating devices, and to configure the network.
  Control frames: control the flow of data on the network, such as requesting or acknowledging the transmission of data.
  Data frames: transmit data between devices on the network.
Header | Payload | Trailer(ICV)
802.11 data frame
ICV: Integrity Check Value = cyclic redundancy check (CRC) value
ICV = CRC(Header+ Payload)

## Slide 17: IEEE 802.11 Supports Encryption Protocols
Encryption Protocols
  Wired Equivalent Privacy (WEP),
  Wi-Fi Protected Access (WPA), and
  Wi-Fi Protected Access II (WPA2).
These protocols use various methods to encrypt the data transmitted in 802.11 frames
  symmetric key encryption,
  public key encryption, and
  message authentication codes.
Users can choose to use encryption or not
  depends on the configuration of the network and the security needs of its users.

## Slide 18: Wired Equivalent Privacy (WEP)
It is an outdated security protocol used to protect wireless local area networks (WLANs).
It was one of the first security standards developed for wireless networks and was intended to provide a level of security comparable to that of a wired network.
WEP is stream cipher using RC4 to generate a keystream
WEP key length -64/128/256 bits
  128-bit WEP remains one of the most common implementations

## Slide 19: RC4 Algorithm
RC4 Keystream Generator
RC4 Key
Keystream
XOR
Plaintext
Ciphertext
XOR
Plaintext
RC4 Keystream Generator
RC4 Key
Keystream

## Slide 20: RC4 Keystream Generator
Initialization/key scheduling
  The key is used to initialize a 256-byte state array (S) with the values 0 to 255.
  The state array is then shuffled based on the key.
Keystream generation
  At each step, the generator uses two index variables, i and j, to generate a keystream byte.
    The i-th and j-th elements of the state array are swapped, and
    the sum of i and the j-th element is used to determine the next keystream byte.
  This process is repeated until enough keystream bytes have been generated to encrypt the plaintext.

## Slide 21
# Harry Sauers | 
# rc4.py | 
# demo of RC4 encryption algorithm | 
def key_scheduling(key): | def stream_generation(sched):
sched = [i for i in range(0, 256)] | stream = []
 | i = 0
i = 0 | j = 0
for j in range(0, 256): | while True:
i = (i + sched[j] + key[j % len(key)]) % 256 | i = (1 + i) % 256
 | j = (sched[i] + j) % 256
tmp = sched[j] | 
sched[j] = sched[i] | tmp = sched[j]
sched[i] = tmp | sched[j] = sched[i]
 | sched[i] = tmp
return sched | yield sched[(sched[i] + sched[j]) % 256]
Notes: https://gist.github.com/hsauers5/491f9dde975f1eaa97103427eda50071

## Slide 22: XOR stream cipher
1010 | 1100 | … | … | 1110 | 0101
1110 | 0100 | … | … | 1000 | 1001
keystream
0100 | 1000 | … | … | 0110 | 1100
RC4
=
802.11 WEP data frame
Unencrypted 802.11 data frame

## Slide 23
https://flylib.com/books/en/2.519.1/wep_cryptographic_operations.html
WEP also allows for multiple keys to be stored and used at the same time.
  Specifically, WEP allows for four different keys to be stored simultaneously, and the user can switch between the keys at any time.
This allows for greater flexibility in managing the security of a wireless network.

## Slide 24
Header | Payload | ICV
Header | IV | Key# | Payload | ICV
RC4
Initialization Vector (IV) (24 bits) | Secret Key (40 bits)
Keystream
Unencrypted 802.11 data frame
802.11 WEP data frame
=
64-bit WEP (WEP-40)
seed
Generated by a cryptographically secure random number generator
Ensure that the same key is not used for multiple transmissions.
Multiple keys will be generated, Key# specifies the key that should be used to encrypt and decrypt the data in the frame (8 bits)
generated from password

## Slide 25: Secret Key Management
Secret keys are generated with a passphrase/password
  one passphrase generates multiple keys
Multiple keys provide additional security
  if an attacker were to capture and crack one key, other keys would still be in use
Keys are manually distributed
Every device on the network uses one key to encrypt every transmitted packet
  an eavesdropper could intercept the WEP encryption and find the key.
5 ASCII characters (0–9, a–z, A–Z)
128-bit WEP
WEP 104: 13 ASCII characters (0–9, a–z, A–Z)
Notes: https://www.tech-faq.com/wep-key-passphrase.html

## Slide 27: How Are WEP-40 Secret Keys Generated?
M
y
P
a
s
s
p
h
r
a
s
e
seed
32-bit PRNG
34
a4
a9
27
ee
3d
7b
f7
ab
f6
35
59
12
f3
a3
98
62
74
f3
7f
6a
8e
a3
59
. . .
20 iterations
32 bits (little endian)
32 bits
http://www.blackhat.com/presentations/bh-usa-01/TimNewsham/bh-usa-01-Tim-Newsham.ppt
key 1
a4
f6
f3
74
3d
key 2
key 3
key 4
Seeding: ASCII string mapped to 32-bits
PRNG: Generate 32-bits key candidates
Pseudo Random Number generator (PRNG)
?
Notes: http://alumni.cs.ucr.edu/~nsoracco/tomsnetworking-wepcracking.pdf

## Slide 28: How to find password
40 Bits Security key
Seed
Wifi Password

## Slide 29: WEP-40 Secret Keys Generator has a security problem
WEP-40 security key should have 40-bits of entropy
Key entropy is reduced in several ways
  seed entropy reduced
  PRNG entropy reduced

## Slide 30: Seeding problem – reduced seed entropy (32-28 bits)
XOR operation guarantees produce four zero bits
  Input is ASCII. High bit of each character is always zero
XOR of these high bits is also zero
  Only seeds 00:00:00:00 through 7f:7f:7f:7f can occur (entropy is reduced to 28 bits =32-4)
M
y
P
a
s
s
p
h
r
a
s
e
a 32-bit seed
M | 0 | 1001101
a | 0 | 1100001
h | 0 | 1101000
e | 0 | 1100101
 | 0 | 

## Slide 31: PRNG problem: Reduced PRNG Entropy (32-24 bits)
PRNG is a Linear congruential generator
https://en.wikipedia.org/wiki/Linear_congruential_generator
m=224
32-bit PRNG
34
a4
a9
27
ee
3d
7b
f7
ab
f6
35
59
12
f3
a3
98
62
74
f3
7f
5 iterations
key 1
a4
f6
f3
74
3d
Because the most significant byte of the outputs is not used, which is equivalent to generating only 24-bits words at each iteration.
Only seeds 00:00:00:00 through 00:ff:ff:ff (24 bits) may result in unique keys!
Why not using m=232
Notes: https://en.wikipedia.org/wiki/Linear_congruential_generator

## Slide 32: Find a seed
x0=seed (We want to figure it out)
a=0x000343fd (how do we know, next slide)
c=0x269ec3 (how do we know)
m=0x00FFFFFF (224)
a4
3d
f6
f3
74
32-bit PRNG
5 iterations
?
we know
Approach: Generate 5 candidate keys, x1, x2, x3, x4, x5, their second most significant bytes must match the secret keys. The x1 is the seed

## Slide 33
Notes: https://en.wikipedia.org/wiki/Linear_congruential_generator

## Slide 34
0
1
2
3
4
5
6
7
8
9
10
11
12
6b
76
12
??
32 bits (little endian)
Password Position
We know the password = [A-Za-z]+
https://raw.githubusercontent.com/frankwxu/digital-forensics-lab/main/Illegal_Possession_Images/lab_files/wlan_decrypt/findseed.py
32 bits seed
Notes: key=[0xa4,0x3d,0xf6,0xf3,0x74]
a, c, m = 0x000343fd, 0x269ec3, 0xFFFFFF
secret_key_bytes=5
for seed in range(1<<24):
correct = True
x = seed
for i in range(secret_key_bytes):
x = (a * x + c) & m
# shift 16 bits to right
# the same as check the second most significant byte
if (x>>16)!=key[i]:
correct = False
break
if correct:
print("Found it: ", hex(seed))
print("Verify: ")
for i in range(secret_key_bytes):
seed = (a* seed + c) & m
print(hex(seed>>16),hex(seed))

## Slide 35: How long is the passphrase?
0
1
2
3
4
5
6
7
8
9
10
11
12
6b
76
12
??
32 bits (little endian)
Position
0x12=0001,0010 can only be generated by an even number of [A-Za-z] characters. Why?
If generated by an odd number of [A-Aa-z], 0 should be 1.
Possible passphrase char ends at (include) 9, 17, 25, etc,
How about 0x76 = 0111,0101
 | 9 |  | 
 | 17 |  | 
 | 25 |  | 
 | … |  | 
even #
Notes: https://www.intel.com/content/dam/www/program/education/us/en/documents/the-journery-inside/digital/tji-digital-info-handout4.pdf

## Slide 36: The length of the passphrase is 10
0
1
2
3
4
5
6
7
8
9
6b
76
12
??
Can be any two characters
We only need to brute-force 8 characters.
  All possibility combinations = 528
The hash of the 10-character needs to match the hint provided in the game 0xff7b948953ac.

## Slide 37: Information for cracking passphrase
We know the 40-bit secret key.
  It can be computed by capturing and analyzing WEP packets
  We will demonstrate it later
We know the seed of the secret key
The passphrase consists of all lowercase
  Analyzing the seed
We know the hash code of the passphrase 0xff7b948953ac
  it is provided by CTF
a4
f6
f3
74
3d
6b
76
12
??

## Slide 38
0
1
2
3
4
5
6
7
8
9
6b
76
12
??

## Slide 39
wget https://raw.githubusercontent.com/frankwxu/digital-forensics-lab/main/Illegal_Possession_Images/lab_files/wlan_decrypt/crackWEP40_noGPU_Improved_v1.py
python crackWEP40_noGPU_Improved_v1.py

## Slide 40: Assignment
What are the IP addresses of the host and server?
What are the Mac addresses?
Can you manually extract pictures and HTML pages?
What is the password of the router?

## Slide 41: To do
It seems Wireshark can crack 40-bit secret key

## Slide 42
Decrypt using Wireshark is not working, not sure why

## Slide 43
Notes: A4:3D:F6:F3:74